## Slide 1: OSPFv3
John Rullan Cisco Certified Instructor Trainer Thomas A. Edison CTE HS Stephen Lynch
Network Architect, CCIE #36243
ABS Technology Architects

## Slide 2: How Does OSPF Work?
OSPF is a link-state routing protocol, which is a routing protocol that makes its routing decisions based on the state of the links that connect source and destination devices.
The interface information includes the IPv6 prefix on the interface, the type of network it is connected to, and the routers connected to that network.
OSPF routers generate routing updates only when a change occurs in the network topology.
When a link changes state, the device that detects the change creates an LSA and forwards it to the DR using FF02::6 multicast address who informs all devices within an area using FF02::5 multicast address. Each device then updates its Link State Database.

## Slide 3: OSPFv2
Advertises IPv4 routes.
OSPF messages are sourced from the IPv4 address of the exit interface.
Uses 224.0.0.6 as the DR/BDR multicast address and the 224.0.0.5 all OSPF router multicast address.
Advertises networks using the network command in router configuration mode.
Interfaces are indirectly enabled using the router configuration mode.
Advertises IPv6 routes.
OSPF messages are sourced using the link-local address of the exit interface.
Uses FF02::6 as the DR/BDR multicast address and the FF02::5 all OSPF router multicast address.
The ipv6 ospf process-id area area-id command will enable the routing process and its associated configuration to be created but network statements are no longer used.
Each interface must be enabled using the ipv6 ospf process-id area area-id in interface-configuration mode.
OSPFv3

## Slide 4: Link-state Advertisements
Type | Name | Description
1 | Router LSA | Created by every router and flooded within a single area only. It describes the link state and costs of a router’s links to the area. Sent to the DR in a NBMA.
2 | Network LSA | Describes the link-state and cost information for all routers attached to the network. This LSA is an aggregation of all the link-state and cost information in the network. Only a designated router tracks this information and can generate a network LSA.
3 | Summary LSA | Advertises internal networks to routers in other areas. Type 3 LSAs may represent a single network or a set of networks summarized into one advertisement. Only ABRs generate summary LSAs.
5 | External LSA | Redistributes routes from another AS, usually from a different routing protocol into OSPFv3. A default route is propagated through the OSPF AS as an external network.
Notes: Every router in an area advertises its links to the DR using a type 1 LSA, The DR then informs all of the routers in the area about every other router using a type 2 LSA. Type 3 LSAs are used by the Area Border Router (ABR) to advertise networks from other areas. Type 5 LSAs are used by the Autonomous System Border Router (ASBR) to identify routes external to OSPF. A default route is a perfect example of a type 5 LSA.

## Slide 5: 为什么要使用多区域OSPF? OSPF 两级区域层次
多区域OSPF被布署为两级区域层次:
骨干 (传输)区域
    该区域的功能是快速高效地传输IP 包
    与其他类型OSPF区域互连
    Area 0 （区域0）即为OSPF的骨干区域，需要与所有其他区域直接互连
常规 (非骨干) 区域
    连接用户和资源
    常规区域不允许流量从其他区域通过它到达另外区域
Notes: 8.1.1.3

## Slide 6: 为什么要使用多区域OSPF? OSPF路由器类型
骨干区域
常规区域
Notes: 8.1.1.4

## Slide 7: 为什么要使用多区域OSPF? OSPF路由器的类型
内部路由器
骨干路由器
区域边界路由器（ABR）
自治系统边界路由器（ASBR）
Notes: 8.1.1.4

## Slide 8: 多区域OSPF LSA 运作 OSPF LSA 类型
最常见类型
Notes: 8.1.2.1

## Slide 9: 多区域OSPF LSA 运作 OSPF LSA类型1
1类 LSA:
  包括直连网络前缀和链路类型。
  所有路由器均会产生1类 LSA。
  只在区域内泛洪，不穿越ABR传播。
  链路状态 ID 由产生该路由的路由器 ID来标识。
Notes: 8.1.2.2

## Slide 10: 多区域OSPF LSA 运作 OSPF LSA 类型2
2类 LSA
  标示多路访问链路的路由器和网络地址。
  只有DR路由器产生2类 LSA。
  仅在多路访问区域泛洪，不穿越ABR传播。
  2类LSA 链路状态ID由DR路由器 ID标识。
Notes: 8.1.2.3

## Slide 11: 多区域OSPF LSA 运作 OSPF LSA 类型3
3类 LSA
  描述从1类LSA学习到的网络地址。
  需要为每一个子网通告。
  ABR路由器泛洪3类LSA到其它区域，由其它的ABR再生。
  链路状态 ID 由网络地址标识。
  默认情况下， 路由是不汇总的。
Notes: 8.1.2.4

## Slide 12: 多区域OSPF LSA 运作 OSPF LSA 类型4
4类 LSA
  通告ASBR位置到其它区域并且提供一条路由到达该ASBR。
  ABR 产生4类LSA。
  由始发的ABR产生并由其他的 ABR再生。
  链路状态 ID 由ASBR的路由器ID 标识
Notes: 8.1.2.5

## Slide 13: 多区域OSPF LSA 运作 OSPF LSA 类型5
5类 LSA
  用来通告外部的 (比如非OSPF) 网络地址。
  5类 LSA由 ASBR 产生。
  在整个区域内泛洪并且由其它的ABR再生。
  链路状态 ID 由外部网络地址标识。
  默认情况下，路由不汇总。
Notes: 8.1.2.6

## Slide 14: New Link-State Advertisements
LSA Type 8 (Link LSA) – Only sent to other routers connected to the same link. Link LSAs provide the link-local address of the router to all other routers attached to the link, inform other routers attached to the link of a list of prefixes to associate with the link, and allow the router to assert a collection of Options bits to associate with the network LSA originated by the Designated Router on a NBMA link.
LSA Type 9 (Intra-Area Prefix LSA) – A router can originate multiple intra-area-prefix LSAs for each router or transit network, each with a unique link-state ID. The link-state ID for each intra-area-prefix LSA describes its association to either the router LSA or the network LSA and contains prefixes for stub and transit networks.
Notes: 链路LSA(Link-LSA)：该类型LSA仅在本链路上传播，具有以下3种目的：向本链路上的其它路由器提供路由器的本链路地址;向本链路上的其它路由器通告IPv6地址前缀，使其与本链路相关联;允许路由器在该类型LSA中插入一些选项比特，与为本链路产生的网络LSA相关联
区域内前缀LSA(Intra-Area-Prefix-LSA)：该类型LSA在本区域内传播，具有以下两种功能之一：通过参考网络LSA把IPv6地址前缀与转递网络(transit network)相关联;或者通过参考路由器LSA把IPv6地址前缀与路由器相关联。一台路由器可以为给定的区域产生多个该类型的LSA，这些LSA使用链路状态ID字段(Link State ID)区分。DR为它所代表的链路产生一个或多个该类型的LSA，向整个区域内通告该链路的地址前缀。
These are additional LSAs used only with OSPFv3.

## Slide 15: LSA Type 8 (Link LSA)
Branch-2# show ipv6 ospf database
OSPF Router with ID (2.2.2.2) (Process ID 1)
Router Link States (Area 0)
ADV Router Age Seq# Fragment ID Link count Bits
2.2.2.2 127 0x80000002 0 1 B
1.1.1.1 127 0x80000002 0 1
Inter Area Prefix Link States (Area 0)
ADV Router Age Seq# Metric Prefix
2.2.2.2 132 0x80000001 1 2001:DB8:A::/64
Link (Type-8) Link States (Area 0)
ADV Router Age Seq# Link ID Interface
2.2.2.2 127 0x80000002 4 Se0/0/1
1.1.1.1 128 0x80000002 3 Se0/0/0
Intra Area Prefix Link States (Area 0)
ADV Router Age Seq# Link ID Ref-lstype Ref-LSID
2.2.2.2 128 0x80000001 2 0x2001 0
1.1.1.1 136 0x80000001 2 0x2001 0
OSPF Router with ID (2.2.2.2) (Process ID 1)
Notes: Here is the output of the show ipv6 ospf database command which displays the new LSAs. Here it lists the advertising routers as 2.2.2.2 and 1.1.1.1. Even though OSPFv3 is used for IPv6, notice how the IPv4 router ID is used to identify the OSPFv3 routers.

## Slide 16: Configuration Requirements
Branch-1
S0/0/0
S0/0/1
G0/0
G0/0
2001:DB8:1::/64
2001:DB8:A::/64
Lo0 2001:DB8:C::/127
Lo0 2001:DB8:B::/127
OSPFv3 configuration requirements:
Enable IPv6 unicast routing
Enable the OSPFv3 routing process
Enable OSPFv3 on the interface
Configure passive interfaces
G0/0
Branch-2
Branch-3
Branch-4
Notes: Read slide

## Slide 17: OSPFv3 Configuration
IPv4 packet forwarding is enabled by default, whereas IPv6 packet forwarding is disabled by default.
To enable IPv6 packet forwarding, use the ipv6 unicast-routing command in global configuration mode before enabling OSPF.
Once IPv6 packet forwarding is enabled, we can now enable the IPv6 OSPF routing process.
OSPFv3 continues to use an IPv4 32-bit address for the router ID. Because there are no IPv4 addresses configured on the routers, you are required to manually assign the router ID using the router-id command.
Branch-1
S0/0/0
S0/0/1
G0/0
G0/0
2001:DB8:1::/64
2001:DB8:A::/64
Lo0 2001:DB8:C::/127
Lo0 2001:DB8:B::/127
G0/0
Branch-2
Branch-3
Branch-4
Notes: Read slide

## Slide 18: OSPFv3 Configuration
Branch-2(config)# ipv6 router ospf 1
% IPv6 routing not enabled
Branch-2(config)# ipv6 unicast-routing
Branch_2(config)# ipv6 router ospf 1
%OSPFv3-4-NORTRID: OSPFv3 process 1 could not pick a router-id,please configure manually
Branch-2(config-rtr)# router-id 2.2.2.2
Branch-2(config-rtr)#
Branch-1
S0/0/0
S0/0/1
G0/0
G0/0
2001:DB8:1::/64
2001:DB8:A::/64
Lo0 2001:DB8:C::/127
Lo0 2001:DB8:B::/127
G0/0
Branch-2
Branch-3
Branch-4
RID: 1.1.1.1
RID: 2.2.2.2
Notes: IPv6 unicast routing must be enabled before OSPF can be configured. In
OSPFv3 and OSPFv2, the router uses the 32-bit IPv4 address to select the router ID for an OSPF
process. If an IPv4 address exists when OSPFv3 is enabled on an interface, then that IPv4 address is used
for the router ID. If more than one IPv4 address is available, a router ID is chosen using the same rules
as for OSPFv2. If no IPv4 addresses are configured, the router prompts you to manually configure one. Each router ID must be unique.

## Slide 19: OSPFv3 Configuration
Enabling OSPFv3 with ipv6 ospf process-id area area-id will enable the routing process and its associated configuration to be created.
Unlike OSPFv2, you do not enter network statements. Each interface must be enabled using ipv6 ospf process-id area area-id in interface-configuration mode.
Branch-2(config)# int s0/0/1
Branch-2(config-if)# ipv6 ospf 1area 0
Branch-1
S0/0/0
S0/0/1
G0/0
G0/0
2001:DB8:1::/64
2001:DB8:A::/64
Lo0 2001:DB8:C::/127
Lo0 2001:DB8:B::/127
G0/0
Branch-2
Branch-3
Branch-4
Notes: Read slide

## Slide 20: Configuration Example
Branch_2(config)# ipv6 router ospf 1
Branch_2(config-rtr)# router-id 2.2.2.2
Branch_2(config)# int s0/0/1
Branch_2(config-if)# ipv6 ospf 1 area 1
Branch_2(config-if)# int g0/0
Branch_2(config-if)# ipv6 ospf 1 area 0
00:26:56: %OSPFv3-5-ADJCHG: Process 1, Nbr 1.1.1.1 on Serial0/0/1 from LOADING to FULL, Loading Done
Branch_2(config-if)#
Branch-1
S0/0/0
S0/0/1
G0/0
G0/0
2001:DB8:1::/64
2001:DB8:A::/64
Lo0 2001:DB8:C::/127
Lo0 2001:DB8:B::/127
G0/0
Branch-2
Branch-3
Branch-4
RID: 1.1.1.1
RID: 2.2.2.2
Notes: Once OSPF is enabled on Branch-2 S0/0/0, a log message appears informing you that OSPFv3 has created an adjacency with 1.1.1.1 who in this case is Branch-1.

## Slide 21: Passive Interface
Branch-1
Branch-2
LAN-1
LAN-2
S0/0/0
S0/0/0
G0/0
G0/1
2001:DB8:A::/64
2001:DB8:B::/64
2001:DB8:C::/64
The purpose of the passive interface command is to suppress routing updates out of an interface. With regards to OSPF, it prevents the paranoid update and LSAs from being sent across LANs.
The networks will still be advertised to neighboring routers but routing updates and LSAs will not be forwarded.
Branch-1(config)# ipv6 router ospf 1
Branch-1(config-rtr)# passive-interface g0/0
Branch-1(config-rtr)# passive-interface g0/1
Notes: Passive interface does not appear in the show ipv6 protocols command. It is only displayed in the running configuration.

## Slide 22: Passive Interface
Branch-1
Branch-2
LAN-1
LAN-2
S0/0/0
S0/0/0
G0/0
G0/1
2001:DB8:A::/64
2001:DB8:B::/64
2001:DB8:C::/64
Branch-2#show ipv6 ospf interface g0/1
GigabitEthernet0/1 is up, line protocol is up
Link Local Address FE80::202:17FF:FEC2:B902 , Interface ID 2
Area 0, Process ID 1, Instance ID 0, Router ID 2.2.2.2
Network Type BROADCAST, Cost: 1
Transmit Delay is 1 sec, State DR, Priority 1
Designated Router (ID) 2.2.2.2, local address FE80::202:17FF:FEC2:B902
No backup designated router on this network
Timer intervals configured, Hello 10, Dead 40, Wait 40, Retransmit 5
No Hellos (Passive interface)
Index 3/3, flood queue length 0
Next 0x0(0)/0x0(0)
Last flood scan length is 1, maximum is 1
Last flood scan time is 0 msec, maximum is 0 msec
Neighbor Count is 0, Adjacent neighbor count is 0
Suppress hello for 0 neighbor(s)
Branch-2#show ipv6 protocol
IPv6 Routing Protocol is "connected"
IPv6 Routing Protocol is "static
IPv6 Routing Protocol is "ospf 1"
Interfaces (Area 0)
GigabitEthernet0/0
GigabitEthernet0/1
Serial0/0/1
Passive interface does not appear in the show ipv6 protocols command. The show ipv6 ospf interface command verifies that passive interface was configured.
Notes: Passive interface does not appear in the show ipv6 protocols command as it does using the show ip protocols for IPv4. It is only displayed in the running configuration.

## Slide 23: OSPFv3 Verification
Branch-1
S0/0/0
S0/0/1
G0/0
G0/0
2001:DB8:1::/64
2001:DB8:A::/64
Lo0 2001:DB8:C::/127
Lo0 2001:DB8:B::/127
G0/0
Branch-2
Branch-3
Branch-4
There are various show commands that can be used to verify and display OSPFv3 configurations:
Show ipv6 ospf neighbor
Show ipv6 ospf database
Show ipv6 route
Show ipv6 protocols

## Slide 24: OSPFv3 Verification
Branch-1
S0/0/0
S0/0/1
G0/0
G0/0
2001:DB8:1::/64
2001:DB8:A::/64
Lo0 2001:DB8:C::/127
Lo0 2001:DB8:B::/127
G0/0
Branch-2
Branch-3
Branch-4
Branch-2#show ipv6 ospf neighbor
Neighbor ID Pri State Dead Time Interface ID Interface
4.4.4.4 1 FULL/BDR 00:00:36 1 GigabitEthernet0/0
3.3.3.3 1 FULL/DROTHER 00:00:33 1 GigabitEthernet0/0
1.1.1.1 0 FULL/ - 00:00:37 3 Serial0/0/1
Neighbor’s IPv6 ID
State
Expected time before Cisco IOS software will declare the neighbor dead.
Every interface is assigned an Interface ID, which uniquely identifies the interface with the router.
Priority
Notes: OSPF priority of 0 is automatically assigned to point-to-point serial connection whereas a priority of 1 is the default priority for NBMA networks.
With the OSPF state, there is no DR/BDR election on serial interfaces therefore no designation is listed.

## Slide 25: OSPFv3 Verification
Branch-1#show ipv6 route
(Output Omitted)
IPv6 Routing Table - 4 entries
Codes: C - Connected, L – Local
O - OSPF intra, OI - OSPF inter, OE1 - OSPF ext 1, OE2 - OSPF ext 2
C 2001:DB8:1::/64 [0/0]
via ::, Serial0/0/0
L 2001:DB8:1::/128 [0/0]
via ::, Serial0/0/0
O 2001:DB8:A::/64 [110/65]
via FE80::2E0:8FFF:FE0A:5302, Serial0/0/0
L FF00::/8 [0/0]
via ::, Null0
Branch-1#
In Branch-1’s routing table, it indicates
that a route has been learned through OSPF and S0/0/0 is the exit interface to reach the address.

## Slide 26: Multi-area OSPFv3

## Slide 27: Multi-area OSPFv3
Backbone area (Area 0) – OSPF has special restrictions when multiple areas are involved. If more than one area is configured, one of these areas has be to be area 0. All areas have to be physically connected to the backbone. The reasoning behind this is that OSPF expects all areas to inject routing information into the backbone and in turn the backbone will disseminate that information into other areas.
Regular (non-backbone) area – Connects users and resources. Regular areas are usually set up along functional or geographical groupings. By default, a regular area does not allow traffic from another area to use its links to reach other areas. All traffic from other areas must cross through area 0.

## Slide 28: OSPF Router Types
There are 4 types of OSPF routers.
  - Internal Router (IR) – A router that has every interface in the same area.
  Area Border Router (ABR) – A router that has an interface in multiple areas and generates summary LSAs. It connects one or more areas to the main backbone network.
  Autonomous System Border Router (ASBR) – A router that is connected to more than one routing protocol or has at least one interface outside of OSPF. Used to distribute routes received from other, external LSAs throughout its own autonomous system.
  Backbone Router (BR) – A router that is connected to the backbone area.

## Slide 29: OSPFv3 Multi-area Configuration
Branch-1
S0/0/0
S0/0/1
G0/0
G0/0
2001:DB8:1::/64
2001:DB8:A::/64
Lo0 2001:DB8:C::/127
Lo0 2001:DB8:B::/127
G0/0
Branch-2
Branch-3
Branch-4
Area 51
Area 0
Branch-2(config)#int s0/0/1
Branch-2(config-if)#ipv6 ospf 1 area 0
Branch-2(config-if)#int g0/0
Branch-2(config-if)#ipv6 ospf 1 area 51
00:11:25: %OSPFv3-5-ADJCHG: Process 1, Nbr 1.1.1.1 on Serial0/0/1 from LOADING to FULL, Loading Done
Branch-2(config-if)#
00:11:27: %OSPFv3-5-ADJCHG: Process 1, Nbr 3.3.3.3 on GigabitEthernet0/0 from LOADING to FULL, Loading Done
00:11:30: %OSPF-5-ADJCHG: Process 1, Nbr 4.4.4.4 on GigabitEthernet0/0 from FULL to DOWN, Neighbor Down: Dead timer expired
00:11:30: %OSPFv3-5-ADJCHG: Process 1, Nbr 4.4.4.4 on GigabitEthernet0/0 from FULL to DOWN, Neighbor Down: Interface down or detached
Notes: Once OSPF is enabled on Branch-2 S0/0/0, it created an adjacency with Branch-1.

## Slide 30: OSPFv3 Multi-area Verification
Branch-2# show ipv6 ospf database
OSPF Router with ID (2.2.2.2) (Process ID 1)
Router Link States (Area 0)
ADV Router Age Seq# Fragment ID Link count Bits
2.2.2.2 291 0x80000003 0 1 B
1.1.1.1 292 0x80000003 0 1
Inter Area Prefix Link States (Area 0)
ADV Router Age Seq# Metric Prefix
2.2.2.2 296 0x80000002 1 2001:DB8:A::/64
Link (Type-8) Link States (Area 0)
ADV Router Age Seq# Link ID Interface
2.2.2.2 291 0x80000003 4 Se0/0/1
1.1.1.1 293 0x80000003 3 Se0/0/0
Intra Area Prefix Link States (Area 0)
ADV Router Age Seq# Link ID Ref-lstype Ref-LSID
2.2.2.2 292 0x80000002 2 0x2001 0
1.1.1.1 300 0x80000002 2 0x2001 0
OSPF Router with ID (2.2.2.2) (Process ID 1)
Router Link States (Area 51)
ADV Router Age Seq# Fragment ID Link count Bits
2.2.2.2 261 0x80000004 0 1 B
3.3.3.3 262 0x80000003 0 1
Net Link States (Area 51)
ADV Router Age Seq# Link ID (DR) Rtr count
3.3.3.3 262 0x80000002 1 2
Inter Area Prefix Link States (Area 51)
ADV Router Age Seq# Metric Prefix
2.2.2.2 286 0x80000002 64 2001:DB8:1::/64
Link (Type-8) Link States (Area 51)
ADV Router Age Seq# Link ID Interface
2.2.2.2 271 0x80000003 1 Gi0/0
3.3.3.3 262 0x80000003 1 Gi0/0
Intra Area Prefix Link States (Area 51)
ADV Router Age Seq# Link ID Ref-lstype Ref-LSID
2.2.2.2 300 0x80000002 2 0x2001 0
3.3.3.3 300 0x80000003 2 0x2001 0
3.3.3.3 262 0x80000004 1 0x2002 1
Branch-2#